## Slide 1: Hybrid Decentralization for Multi-Robot Orienteering with Mothership-Passenger Systems
Nathan L. Butler and Geoffrey A. Hollinger
Robotics Program, School of Mechanical, Industrial, and Manufacturing Engineering
Oregon State University
NSF Award No.
2322055

## Slide 2
In this work, we leverage a hybrid centralized-distributed network available in robotic Mothership-Passenger systems to solve complex orienteering problems.

## Slide 3
Ice Shelf
Mothership
We motivate our work with an underwater multi-robot system designed to explore polar ice shelves.

## Slide 4
Mothership
We consider this reduced network topology

## Slide 5
Mothership
Centralized Topology
The Mothership may be thought of as a centralized controller, capable of sending commands to each Passenger

## Slide 6
Mothership
Distributed Topology
The Passengers may be considered as a distributed network, capable of sharing information between themselves and the Mothership

## Slide 7
Mothership
Passenger i
UpdateScheduleDists
Neighboring Passengers
Task Data
Mothership
STOP & SOP Solver
(Sim-BRVNS)
SOP Solver
(MCTS)
Task Data
Hybrid Rescheduling
We introduce the hybrid tour scheduling algorithm for Passenger orienteering.

## Slide 8
Mothership
Hybrid Rescheduling
Passenger i
UpdateScheduleDists
Neighboring Passengers
Task Data
Mothership
STOP & SOP Solver
(Sim-BRVNS)
SOP Solver
(MCTS)
Task Data
The algorithm exchanges scheduling information between Passengers and the Mothership to create new tours as follows.

## Slide 9
Mothership
Hybrid Rescheduling
Request new schedule from Mothership
A Passenger attempts to request a new tour plan from the Mothership

## Slide 10
Mothership
Hybrid Rescheduling
Mothership creates schedule with Sim-BRVNS solver
If Message Received:
Request new schedule from Mothership
The Mothership uses a powerful onboard solver and leverages information it has aggregated to develop a new tour.

## Slide 11
Mothership
Hybrid Rescheduling
Mothership sends new schedule to Passenger
Mothership creates schedule with Sim-BRVNS solver
If Message Received:
Request new schedule from Mothership
The Mothership attempts to return the new tour to the Passenger

## Slide 12
Mothership
Hybrid Rescheduling
If Message Received:
Begin executing new schedule, share updated schedule distribution
Mothership sends new schedule to Passenger
Mothership creates schedule with Sim-BRVNS solver
If Message Received:
Request new schedule from Mothership
If received, the Passenger begins to execute the new tour and communicates its new plan to neighboring robots.

## Slide 13
Mothership
Hybrid Rescheduling
If no schedule from Mothership:
Solve set of local schedules with MCTS
Otherwise, the Passenger uses a local solver to create a set of possible tours given locally-available information.

## Slide 14
Mothership
Hybrid Rescheduling
If no schedule from Mothership:
Solve set of local schedules with MCTS
Evaluate MCTS solutions and stored schedules, select best-performing subset
The Passenger compares its new tours to a set of previously-solved tours, evaluating reward and reliability.

## Slide 15
Mothership
Hybrid Rescheduling
If no schedule from Mothership:
Solve set of local schedules with MCTS
Evaluate MCTS solutions and stored schedules, select best-performing subset
Begin executing best schedule, share updated schedule distribution
The Passenger generates a schedule distribution with the top-performing schedules and communicates this to neighbors. It then begins executing the best-performing schedule.

## Slide 16
With this hybrid framework, Passengers with strong connections to the Mothership are equipped to operate using well-informed centrally-developed tours while Passengers with strong connections to neighboring Passengers solve tours as a distributed system.

## Slide 17
This enables the system to take advantage of the high-performing solutions generated by a centralized controller while remaining robust to lost connections to the central node.

## Slide 18
Contact:
Nathan Butler: butlnath@oregonstate.edu
Geoffrey Hollinger: geoff.hollinger@oregonstate.edu