## Slide 1
Hybrid Decentralization for Multi-Robot Orienteering with Mothership-Passenger Systems
Nathan L. Butler and Geoffrey A. Hollinger
Collaborative Robotics and Intelligent Systems (CoRIS) Institute, Oregon State University
Hybrid Decentralized Mission Planning
Experiments and Results
Our hybrid planning framework offers an initial performance boost from the mothership’s centralized solver. Once deployed, the mothership improves system-level coordination in the presence of disturbances.
We evaluate our framework in a simulated underwater environment.
Tasks (V) and the mothership location (M) are distributed randomly.
Ocean currents from high-fidelity underwater simulator provide stochastic travel times.
We compare four algorithmic variants:
Initial, centralized solution only (Sim-BRVNS [X])
Decentralized planning only (Dec-MCTS [X])
Initial + decentralized replanning (2-Stage)
Initial + hybrid replanning (2-Stage Hybrid)
We inject disturbances (robot failures, new tasks) into the system to evaluate each method’s replanning performance.
3 Robots, 30 Tasks
6 Robots, 20 Tasks
We inject plans developed by a powerful centralized planner onboard the mothership into passengers’ decentralized planning routines to improve system-level coordination.
Multi-robot teams are useful for efficiently exploring isolated, hazardous environments.
If reaching the environment is itself a hazardous task, a larger mothership robot can be used to first transport the team to regions of interest.
Once the team has been deployed, passengers must solve a challenging Stochastic Multiagent Orienteering Problem to allocate tasks, plan paths, and return to the mothership for extraction within battery limits.
Opportunity: How can we leverage a hybrid centralized-decentralized network available in Mothership-Passenger systems to solve complex orienteering problems?
NSF Award
#2322055
QR TO WEBSITE PAPER
butlnath@oregonstate.edu
natbut.github.io