## Slide 1
Hybrid Decentralization for Multi-Robot Orienteering with Mothership-Passenger Systems
Nathan L. Butler and Geoffrey A. Hollinger
Collaborative Robotics and Intelligent Systems (CoRIS) Institute, Oregon State University
Hybrid Decentralized Mission Planning
Our hybrid planning framework offers an initial performance boost from the mothership’s centralized solver. Global coordination provided by the mothership improves system robustness in high-disturbance scenarios.
We evaluate our framework in a simulated underwater environment.
Tasks (T) and the mothership location (M) are distributed randomly.
Ocean currents from high-fidelity underwater simulator introduce stochastic travel costs.
We compare four algorithmic variants:
Offline, centralized solution only
Decentralized planning only
Offline + decentralized replanning
Offline + hybrid replanning
We inject disturbances (robot failures, new tasks) at specified rates into the system.
These disturbances introduce heterogeneity in team observations and allow us to evaluate each method’s replanning performance.
3 Robots, 30 Tasks
6 Robots, 20 Tasks
We inject plans created by a powerful centralized planner onboard the mothership into passengers’ decentralized planning routines to improve system-level coordination.
Multi-robot teams can efficiently explore new environments. If reaching the operational domain is itself a dangerous job, a mothership robot can transport the team to regions of interest.
Once deployed, the team must solve a challenging Stochastic Multiagent Orienteering Problem to 1) allocate tasks, 2) plan paths, and 3) return to the mothership for extraction within a travel budget in a stochastic environment.
A multi-robot team solving this problem fully decentralized may struggle to produce globally-coordinated plans if information propagates slowly through the system.
Opportunity: How can we leverage a hybrid centralized-decentralized network available in Mothership-Passenger systems to solve complex orienteering problems?
Acknowledgements: Financial support provided by U.S. National Science Foundation, award #2322055. Special thanks to our collaborators at Arizona State University, Brigham Young University, Purdue University, Temple University, and Woods Hole Oceanographic Institution.
Experiments and Results
Mothership
Centralized Solver
Marine under-ice mission planning
Mothership
Aggregate observations from connected passengers.
Compute joint team plans with centralized solver.
Share solutions with connected passengers.
Passenger i
Plan Valuation & Selection
Decentralized Solver
Candidate Plans
Neighboring Robots
Stored Plans
Solve local plan using observations & candidate plans from neighbors.
Evaluate new plans against stored high-value solutions (both solved locally & received from mothership).
Store & share distribution of high-value plans.
Passengers’ decentralized planning routine supports coordination with neighbors in communication range.
Plans received from the mothership work to align passenger actions with distant robots.
butlnath@oregonstate.edu
natbut.github.io
Sampling-based solvers address environment stochasticity