## Slide 1: Hybrid Decentralization for Multi-Robot Orienteering with Mothership-Passenger Systems
Nathan L. Butler and Geoffrey A. Hollinger
Robotics Program, School of Mechanical, Industrial, and Manufacturing Engineering
Oregon State University
NSF Award No.
2322055

## Slide 2
In this work, we leverage a hybrid centralized-distributed network available in robotic Mothership-Passenger systems to solve complex orienteering problems.

## Slide 3
Mothership
We motivate our work with an underwater multi-robot system designed to explore polar ice shelves.

## Slide 4
Mothership
We consider this reduced network topology

## Slide 5
Mothership
Centralized Topology
The Mothership may be thought of as a centralized controller, capable of sending commands to each Passenger

## Slide 6
Mothership
Distributed Topology
The Passengers may be considered as a distributed network, capable of sharing information between themselves and the Mothership

## Slide 7
Mothership
Hybrid Rescheduling
We introduce the hybrid tour scheduling algorithm for Passenger orienteering.
Passenger i
UpdateScheduleDists
Neighboring Passengers
Task Data
Mothership
STOP & SOP Solver
(Sim-BRVNS)
SOP Solver
(MCTS)
Task Data

## Slide 8
With this hybrid framework, Passengers with strong connections to the Mothership are equipped to operate using well-informed centrally-developed tours while Passengers with strong connections to neighboring Passengers solve tours as a distributed system.
Passenger i
UpdateScheduleDists
Neighboring Passengers
Task Data
Mothership
STOP & SOP Solver
(Sim-BRVNS)
SOP Solver
(MCTS)
Task Data

## Slide 9
This enables the system to take advantage of the high-performing solutions generated by a centralized controller while remaining robust to lost connections with the central node.
Passenger i
UpdateScheduleDists
Neighboring Passengers
Task Data
Mothership
STOP & SOP Solver
(Sim-BRVNS)
SOP Solver
(MCTS)
Task Data

## Slide 10
Simulation Environment
Worker Robots (Blue o)
Support Robots (Green x)
Tasks (Red o)
Planned Tours
Simulated ocean currents cause unpredictable battery loss

## Slide 11
Simulation 1: Baseline Scenario Performance
Dec-MCTS OR Sim-BRVNS
Hybrid
Decentralized Monte Carlo Tree Search
Distributed planning without Mothership
Our Hybrid Rescheduling Algorithm
Initial plan from Mothership
Revised online using hybrid method

## Slide 12
Simulation 2: Replanning with Robot Failures
Tasks originally scheduled for failed robots are integrated into other robots’ plans.

## Slide 13
Simulation 3: Replanning with New Tasks
New tasks are incorporated into robots’ plans online.

## Slide 14
Contact:
Nathan Butler: butlnath@oregonstate.edu
Geoffrey Hollinger: geoff.hollinger@oregonstate.edu